## Slide 1
PHOTO
Aerial view of a large modern distribution centre with trucks at dock doors, UAE desert surroundings
LEARN SCM · FREE FOR EVERYONE
Store
Module 5 · Warehouses, flow and where to put them
Notes: TIMING: 2 min. Welcome back. Ask: "Which supplier risk keeps you up at night?" Take two answers. SAY: "Goods are bought. Now we need somewhere to put them, a way to move them inside the building, and a smart choice of where those buildings sit." PREVIEW: layouts, slotting, automation, and a network design trade-off. PHOTO BOX: Aerial view of a large modern distribution centre with trucks at dock doors, UAE desert surroundings

## Slide 2
Where we are, and where we are going
3 MIN
1
Recap
Suppliers chosen, risks planned
2
Today: Store
Inside the four walls, then the network
3
By the end
Read a warehouse flow and slot items sensibly
4
You will do
Slot a pick face, then place a DC
Notes: TIMING: 3 min. RECAP: Module 4 gave us suppliers and risk plans; Module 3 told us how much to hold. Today is where it physically lives. OUTCOMES: say aloud. ASK: "Who works in or near a warehouse?" Invite them to answer practical questions later.

## Slide 3
WARM-UP · 4 MIN
How much of a picker's day is spent walking?
Type your guess as a percentage.
Notes: TIMING: 4 min. SAY: "A picker collects items for orders. Guess the share of time spent travelling rather than picking." COLLECT answers. Often quoted figure: around half or more of order picker time, according to widely cited warehousing studies. Say "often quoted", not exact. POINT: walking adds cost and no value; layout and slotting attack it directly. KEEP the discussion short.

## Slide 4
Why warehouses exist
4 MIN
Not just storage. A warehouse does four jobs.
Buffer
Smooth the gap between supply and demand.
Consolidate
Combine small shipments into efficient loads.
Serve
Pick, pack and ship in small orders, fast.
Notes: TIMING: 4 min. SAY: "If you think of a warehouse as a shed, you will run it badly. It is a processing centre." BUFFER: ties to Stock. CONSOLIDATE: many suppliers in, one load out (or the reverse). SERVE: the customer promise; speed and accuracy of orders. ADDITIONAL: value-added services such as labelling, kitting, returns handling and light assembly. ASK: "Which of these is your site best at?"

## Slide 5
Types of warehouse
5 MIN
1
Own or private
Full control, fixed cost
2
Public or 3PL
Pay as you use, shared, flexible
3
Bonded and free zone
Duty suspended while goods are inside. UAE examples: JAFZA, KEZAD, Dubai South
4
Distribution centre
Fast movement, high throughput
5
Fulfilment centre
Pick and ship direct to consumers
Notes: TIMING: 5 min. SAY: "Choose by volume, variability, control and customs needs." UAE CONTEXT: free zones and bonded facilities allow goods to be stored without paying import duty until they enter the mainland; it matters for re-export. Customs is Module 7. 3PL: third-party logistics provider, which offers flexibility when demand is uncertain. ASK: "Do you own, lease or outsource? Why?"

## Slide 6
Inside the warehouse: six steps
4 MIN
Every box follows this path.
Receive
Check, count, inspect
Put away
Move to storage
Store
Hold and protect
Pick
Collect for orders
Pack
Box and label
Ship
Load and dispatch
Pick is usually the most expensive step.
Notes: TIMING: 4 min. SAY: "Walk the path of a fryer carton." RECEIVE: check against the advance shipping notice; errors here travel downstream. PUT AWAY: system directed. STORE: protect and track. PICK: the biggest cost and time. PACK: protect, label correctly. SHIP: load plans and documents. LINK: information flow from Module 1; if the system record is wrong, the stock is lost even though it is physically there.

## Slide 7
Layout: how goods flow
5 MIN
Through-flow
Receive at one side, ship at the other. Simple, fast, needs two dock faces.
Best for: high volume
U-flow
Receive and ship on the same side. Shares docks, cross-docking easy.
Best for: compact sites
Short distances and no crossing paths are the aim.
Notes: TIMING: 5 min. SAY: "Draw the path of an order. If it zigzags, fix the layout." PRINCIPLES: minimise travel, avoid crossing flows, keep fast movers near dispatch, leave space for growth and safety. REAL WORLD: existing buildings constrain; adapt principles to what you have. ASK: "Where does congestion happen in your warehouse?" Usually docks and aisle intersections.

## Slide 8
Storage equipment
4 MIN
1
Pallet racking
Standard. Selective access to each pallet
2
Shelving and bins
Small items, high pick rates
3
Drive-in and push-back
Dense, fewer SKUs, less selective
4
Mezzanine
More floor space from vertical room
5
AS/RS
Automated storage and retrieval, high investment
Notes: TIMING: 4 min. SAY: "Match equipment to the product and pick profile." TRADE-OFF: density versus access. Dense systems save space but reduce selectivity. UAE NOTE: high temperatures matter; check product heat limits and warehouse cooling for electronics. SAFETY: racking standards and load limits; involve an engineer. ASK: "What is the oldest equipment still in use at your site?"

## Slide 9
Slotting: where each item lives
5 MIN
Put the right item in the right place.
By speed
Fast movers in the golden zone: near dispatch, waist height.
By size
Heavy and bulky low; light and small high. Match the slot to the pack.
By affinity
Items often ordered together live close to each other.
Notes: TIMING: 5 min. SAY: "Slotting is a cheap way to cut walking. No building needed." GOLDEN ZONE: the easiest-to-reach positions; place A items there. RE-SLOT regularly: demand changes with seasons; Ramadan peaks move the fast movers. LINK: ABC analysis from Stock drives slotting. EXAMPLE: put the top fryer SKU at waist height near the dispatch doors.

## Slide 10
Slot it
ACTIVITY · 6 MIN
Golden zone (G), upper (U), lower (L) or back (B)? Type one letter.
1
Best-selling air fryer, light pick
2
Rarely sold spare heating element
3
Heavy 25 kg commercial fryer
4
Cardboard packing used on every order
Notes: TIMING: 6 min. SUGGESTED ANSWERS: 1 G. 2 B or U (slow mover, small). 3 L (heavy, floor level for safety). 4 G or near packing station. KEY POINT: balance speed, weight and ergonomics. DISCUSSION: ask why not everything in the golden zone? Space is limited.

## Slide 11
Picking methods
4 MIN
How orders get collected.
Piece
One order at a time
Batch
Several orders, one pass
Zone
Each picker owns an area
Wave
Release in timed groups
Match method to order profile: lines per order and volume.
Notes: TIMING: 4 min. SAY: "Pick method changes productivity more than most people expect." PIECE: simple, many orders with many lines. BATCH: many small orders. ZONE: large sites; handoff needed. WAVE: coordinates with carrier cut-offs. EXAMPLE: online fryer orders are often one line, so batch picking can be efficient. ASK: "Which method do you use and why?"

## Slide 12
Technology that helps
5 MIN
1
WMS
Warehouse management system: directs, records and optimises
2
Barcode or RFID
Accurate, fast tracking
3
Pick-to-light and put-to-wall
Lights or displays guide pickers and sorters
4
Robots (AMRs)
Move goods to people or carry totes
5
Automation caution
Great for scale and stable profiles; costly if volumes change
Notes: TIMING: 5 min. SAY: "Fix the process first. Then automate." WMS: the brain. Without accurate data robots do not help. INVESTMENT: payback depends on labour cost and volume. In the UAE, labour costs are lower than in some markets, which can slow automation payback; check your numbers. PROBE: "Which tech has helped you most?" Frequently barcode scanning.

## Slide 13
Cross-docking vs storing
4 MIN
Cross-dock
Goods arrive, are sorted, and leave within hours. Minimal storage.
Needs: predictable flows, good info
Store and pick
Goods are held, then picked to order.
Needs: space, system, inventory cost
Which is right for fast moving fryer accessories?
Notes: TIMING: 4 min. SAY: "Cross-docking cuts holding cost and time but needs coordination." EXAMPLE: inbound container is split by customer or store and sent out the same day. RISKS: late inbound breaks the chain; mistakes ripple fast. TIP: cross-dock the predictable, store the rest. ASK: "Could any of your flows be cross-docked?"

## Slide 14
Measuring a warehouse
4 MIN
A few numbers tell most of the story.
Accuracy
Inventory record vs physical. Aim for very high; every miss is a lost sale or a surprise.
Speed
Dock-to-stock time, order cycle time, pick rate.
Quality
On-time-in-full, damage rate, returns processing time.
Notes: TIMING: 4 min. SAY: "Pick three that matter. Track them weekly." ACCURACY: cycle counts reveal errors early. SPEED: dock-to-stock is a favourite because late put-away hides stock from sales. QUALITY: OTIF (on time, in full) is the customer view. TIP: share the numbers with the team; measurement without feedback does not change behaviour.

## Slide 15
Network design: one or many?
5 MIN
Centralised
One or two big sites. Lower stock, lower fixed cost, longer delivery.
Wins on: cost and stock
Decentralised
Many local sites. Faster delivery, higher stock and cost.
Wins on: speed and service
The answer depends on how fast customers need goods.
Notes: TIMING: 5 min. SAY: "More warehouses means shorter delivery but more safety stock and more fixed cost." SQUARE ROOT LAW: safety stock tends to rise with the square root of the number of sites, so doubling sites does not double stock but it does increase it. UAE EXAMPLE: the UAE is compact, so one well-placed site can reach most customers within a day; a second site may help for peak. ASK: "How fast do your customers need goods?"

## Slide 16
The cost of adding warehouses
5 MIN
Illustrative index: inventory rises, transport falls. Total cost has a low point.
Chart: 
| DCs 1 | DCs 2 | DCs 3 | DCs 4 | DCs 5 | DCs 6
Inventory | 30 | 42 | 52 | 60 | 67 | 73
Transport | 120 | 85 | 69 | 60 | 54 | 49
Facilities | 15 | 30 | 45 | 60 | 75 | 90
Total | 165 | 157 | 166 | 180 | 196 | 212
The right answer moves when your customer promise moves.
Notes: TIMING: 5 min. SAY: "This is a teaching curve, not a real forecast. Inventory rises as you add sites, transport falls, facility cost climbs. The total is lowest around 2 sites in this example." POINT: the low point is flat; do not chase perfection. ASK: "What would shift the best point to the right?" Answers: higher service demands, faster promises, expensive transport. DATA: invented index values, computed from simple formulas for illustration.

## Slide 17
Choosing a location
5 MIN
1
Customers and flows
Where do goods come from, and where do they go?
2
Access
Ports, highways, rail, airports, labour supply
3
Cost
Land, rent, labour, utilities, incentives
4
Rules
Free zone or mainland, customs, licensing
5
Risk
Floods, heat, single-route dependence, geopolitics
Notes: TIMING: 5 min. SAY: "Location is a long-term decision, so test it from several angles." UAE EXAMPLES: Jebel Ali area and Dubai South for port and air access; KEZAD for Abu Dhabi and Khalifa Port; Sharjah for cost. Check current options and rules. RECENT LESSON: access to a single port can be a vulnerability. Several ports and overland routes help; Module 8 returns to this. ASK: "What would you check first?"

## Slide 18
Last mile
4 MIN
The final delivery costs the most per parcel.
Why it costs
Many stops, small drops, failed delivery attempts, traffic and heat.
Options
Own fleet, couriers, lockers, pick-up points, gig drivers.
Trends
Same-day, time slots, route optimisation, electric vans.
Notes: TIMING: 4 min. SAY: "The last mile is often the most expensive and most visible leg." ADDRESSING: many UAE areas lack building-number addresses; delivery often relies on phone calls or location pins, a source of failed first attempts. Verify current local practice. IDEAS: lockers, delivery time windows, cash-on-delivery handling. ASK: "What is your biggest last-mile frustration?"

## Slide 19
TEAM CHALLENGE · 20 MIN
Where should Dune & Co. put its warehouse?
1
Options: Jebel Ali free zone, Sharjah, KEZAD (Abu Dhabi)
2
Pick one or two. Score them on customers, access, cost, risk
3
Say what would change your mind
PHOTO
City map with pins marking potential warehouse locations around Dubai and Abu Dhabi
Notes: TIMING: 20 min (3 brief, 10 work, 7 playback). SETUP: breakout rooms of three or four. Provide: customers spread across Dubai, Sharjah, Abu Dhabi and Northern Emirates; mix of consumer and trade orders; fryers arrive by sea. EXPECT: groups may choose one central site, or a main site plus a small second site; free zone for re-export, mainland for local sales. LISTEN FOR: use of customs, risk and port access; recognising a trade-off. DEBRIEF: ask each group to explain the single biggest reason behind their choice. PHOTO BOX: City map with pins marking potential warehouse locations around Dubai and Abu Dhabi

## Slide 20
Take this with you
4 MIN
1
A warehouse is a process
Receive, put away, store, pick, pack, ship
2
Slot by speed and weight
Cut walking and risk
3
Fix, then automate
Process before robots
4
Network is a trade-off
Speed versus cost versus stock
Notes: TIMING: 4 min. REVISIT THE WARM-UP: "How much walking?" Ask if anyone wants to revise. ASK: one action each. FEEDBACK prompt. THANK the room.

## Slide 21
NEXT: MODULE 6 · MOVE
Stored. Now: how do the goods travel?
Modes, containers, freight rates, forwarders and a quote challenge.
PHOTO
Container ship being loaded alongside stacked containers at a port, dusk
Notes: TIMING: 1 min. SAY: "Next: the movement itself. Modes, containers, who does what, and how the price is built." HOMEWORK (optional): bring one freight quote you received and a question about it. PHOTO BOX: Container ship being loaded alongside stacked containers at a port, dusk